Specifications of Gen-2 Passive Position Sensing Probes, 06/10/2003

Wafer Level Device Count for Mask Set: GP2_SG_JW_0203

Table 1. Devices on GP2_SG_JW_0203

|  | Name | Purpose |
| --- | --- | --- |
|  | gp2_frame_basic | 8 gp2 position sensing probes with basic backend in one frame |
|  | gp2_die_basic | Individual position sensing probes with basic backend |
|  | gp2_frame_newback | 6 gp2 position sensing probes with chronic backend in one frame |
|  | gp2_die_newback | Individual position sensing probes with chronic backend |
|  | gp2_soaktest | A group of 4 soaktest cables |
|  | gp2_sg_test | Test chip |
|  | gp2_align_horizon | Alignment marks |

Gen-2 Position Sensing Array with Standard Backend – In Palette

Gen-2 Position Sensing Array with 32-channel Charonic Backend – In Palette

Specifications for Gen-2 Position Sensing Array with 32-channel Standard Backend

Gp2_allsg_basi & gp2_polyC_basic

- Length of the curvature sensors: 930 µm (poly-Si), 460±10 µm(poly-diamond)

- Distance between two curvature sensors: 1000 µm

- Distance between two upper wall contact  sensors: 2000 µm

- Distance between two lower wall contact sensors: 2000 µm

Specifications for Gen-2 Position Sensing Array with 32-channel Standard Backend (integrated with 8-electrode stimulation arrary)

Gp2_sgsites_basic & gp2_polyC_sgsites_basic

- Length of the curvature sensors: 450 µm (poly-Si), 450 µm(poly-diamond)

- Distance between two curvature sensors: 1000 µm

Specifications for Gen-2 Position Sensing Array with 32-channel Chronic Backend

Gp2_allsg_newBack & gp2_polyC_newBack

- Length of the curvature sensors: 930 µm (poly-Si), 460±10 µm(poly-diamond)

- Distance between two curvature sensors: 1000 µm

- Distance between two upper wall contact  sensors: 2000 µm

- Distance between two lower wall contact sensors: 2000 µm

Specifications for Gen-2 Position Sensing Array with 32-channel Chronic Backend

(integrated with 8-electrode stimulation arrary)

Gp2_sgsites_newBack & gp2_polyC_sgsites_newBack

- Length of the curvature sensors: 450 µm (poly-Si), 450 µm(poly-diamond)

- Distance between two curvature sensors: 1000 µm

Specifications for Electrode Sites

Specifications for Tip Sensor and Wall Contact Sensors

Pin Diagram for Passive MEMS Arrays

gp2_allsg_basic & gp2_polyC_basic

gp2_allsg_newBack & gp2_polyC_newBack

gp2_sgsites_basic & gp2_polyC_sgsites_basic

gp2_sgsites_new Back & gp2_polyC_sgsites_newBack

# Text boxes

Overall Palette Dimension:

Width = 20233 µm

Height = 10065 µm

Thickness = 15 µm

Device Specifications:

Length = 16159 µm

Width

Max = 630 µm

Min = 200 µm

318 µm

346 µm

993 µm

Tether Specifications:

Width = 40 µm

Thickness:

15 µm & 4 µm window for laser cutting

Straight:

Length = 1000 µm

Spacing = 136 µm

Angled:

Length = 1575 µm +220 µm

993 µm

Device Specifications:

Entire length = 13195 µm

Shank:

Length = 10050 µm

Width

Max = 630 µm

Min = 200 µm

Backend:

Length = 3145 µm

Width = 1226 µm

Tether Specifications:

Width = 40 µm

Thickness:

15 µm & 4 µm window for laser cutting

Straight:

Length = 1000 µm

Spacing = 350 µm

Angled:

Length = 1500 µm +220 µm

Overall Palette Dimension:

Width = 17152 µm

Height = 10083 µm

Thickness = 15 µm

183µm

Width=630 µm

1000 µm

950 µm

Piezo-resistor:

Height = 14 µm

Width = 4 µm

630 µm

Tip.

Width at the end = 200 µm

2255 µm

5460 µm

7950 µm

7950 µm

2100 µm

3145 µm

Tip.

Width at the end = 200 µm

630 µm

630 µm

Width=1226 µm

186µm

237 µm

52 µm

18 µm

43 µm

8 µm

0

1

3

2

7

6

5

4

24

25

26

27

28

29

30

31

16

17

18

19

20

21

22

23

15

14

13

12

11

10

9

0

8

15

14

13

12

11

10

9

8

16

17

18

19

20

21

22

23

24

25

26

27

28

29

30

31

7

6

5

4

3

2

1

0

15

14

13

12

11

10

9

8

16

17

18

19

2z0

21

22

23

24

25

26

27

28

29

30

31

7

6

5

4

3

2

1

0

15

14

13

12

11

10

9

8

16

17

18

19

2z0

21

22

23

24

25

26

27

28

29

30

31

7

6

5

4

3

2

1

0

730 µm

300 µm

1750 µm